## Slide 1
Model B End-to-End Pipeline
ETS database
labels 10 Hz
sensor 128 Hz
8 s windows
label: > 50% eating
Quality filter
>= 50% labelled
<= 50% missing
Z-score
per window,
per channel
Input
(1024, 4)
Conv block 1
32 x k9, stride 2
> (256, 32)
Conv block 2
64 x k9, stride 2
> (64, 64)
Conv block 3
64 x k5
> (64, 64)
Channel attention
squeeze-excite
> (64, 64)
Attention pooling
softmax over time
> (64)
Dense + dropout
Dense 64, 0.3
Food head
sigmoid > p(eating)
Threshold
set on validation
participants
Output
eating / not eating
Chew head
training only
count of chews
Loss = BCE(food) + 0.2 x MSE(chews). The chew head is discarded after training.
Notes: Every box maps to a step in the summary tables that follow. Shapes are (time steps, channels). 49,395 trainable parameters with the chew head, 47,282 used at prediction time.

## Slide 2
Model B Summary Table (1/3): Data to Input
Step | Operation | Parameters | Description
1 | Load annotations | study_data.numeric_data, CHGT, BOGT, BIGT at 10 Hz | Reads chew, bout and bite labels for each session, one full day per record. A value of -1 means not annotated.
2 | Define eating per sample | eating = BOGT > 0 or BIGT > 0 | A 10 Hz sample is eating when it falls in a chewing bout or a bite. Samples missing in both are left as -1.
3 | Find the annotated span | first to last non-missing sample | Only the video-annotated part of the day is used. Unannotated time is never treated as not eating.
4 | Load sensor packets | aim_raw_data XYZO, 4 x 1,022 samples per packet | Accelerometer X, Y, Z and optical at 128 Hz. data_timestamp is read as the packet start, as verified by the alignment check.
5 | Place samples on a 128 Hz grid | missing = -1 | Each packet is written at its timestamp. The 2 samples between 1,022-sample packets stay -1, which gives about 99.8% coverage.
6 | Cut windows | 8 s = 1,024 samples | Training uses a 4 s hop (50% overlap). Evaluation uses only the non-overlapping 8 s grid.
7 | Quality filter | keep if >= 50% labelled and <= 50% sensor missing | Drops windows that are mostly unannotated or mostly without sensor data.
8 | Window label | eating if > 50% of labelled samples are eating | One binary label per window, the same majority rule as the AIM-2 paper.
9 | Chew target | count of CHGT marks in the window | Used only by the auxiliary head during training.
10 | Per-window z-score | each channel, each window | Missing samples are excluded, the rest are shifted to mean 0 and scaled to standard deviation 1, and missing samples are then set to 0. No frequency filter is applied.

## Slide 3
Model B Summary Table (2/3): Network
Step | Operation | Parameters | Description
11 | Input | (1024, 4) | 8 s of the four channels.
12 | Conv block 1 | Conv1D 32 filters, kernel 9, stride 2 > BatchNorm > ReLU > MaxPool 2 | Output (256, 32). Learns short local patterns and cuts the sequence by 4. 1,312 parameters.
13 | Conv block 2 | Conv1D 64 filters, kernel 9, stride 2 > BatchNorm > ReLU > MaxPool 2 | Output (64, 64). Longer patterns. 18,752 parameters.
14 | Conv block 3 | Conv1D 64 filters, kernel 5, stride 1 > BatchNorm > ReLU | Output (64, 64). Each of the 64 time steps covers 0.125 s, and each feature sees about 0.9 s of signal, roughly one chew cycle. 20,800 parameters.
15 | Channel attention (squeeze and excitation) | average over time > Dense 16 ReLU > Dense 64 sigmoid > multiply | Scores each of the 64 learned feature channels between 0 and 1 and rescales them. It acts on learned features, not directly on the 4 sensors. 2,128 parameters.
16 | Attention pooling over time | Conv1D 1 x 1 > softmax over 64 steps > weighted sum | Gives each time step a weight and sums the sequence into one 64-value vector, so a short bite is not averaged away. 65 parameters.
17 | Shared dense layer | Dense 64 ReLU > Dropout 0.3 | Combines the pooled features. Dropout reduces overfitting. 4,160 parameters.
18 | Food head | Dense 1 sigmoid | Probability that the window is eating. The only output used for prediction. 65 parameters.
19 | Chew head (training only) | Dense 32 ReLU > Dense 1 softplus | Predicts the scaled chew count. Discarded after training. 2,113 parameters.
Total parameters: 49,395 during training, 47,282 at prediction time.

## Slide 4
Model B Summary Table (3/3): Training and Evaluation
Step | Operation | Parameters | Description
20 | Loss | BCE(food) + 0.2 x MSE(chews) | Chew counts are divided by the 99th percentile of the training participants so both losses sit on a similar scale.
21 | Class balance | weight = total / (2 x class count) | Computed per fold, so neither class can be ignored.
22 | Optimiser | Adam, learning rate 0.001, batch 64 | Standard defaults.
23 | Stopping and schedule | max 80 epochs, early stop patience 12, halve LR after 4 flat epochs, min 1e-5 | Monitors validation loss and restores the best weights.
24 | Cross-validation | leave one subject out, 20 folds | Each participant is tested once by a model that never saw them.
25 | Inner validation | 2 training participants per fold, rotated | Used for early stopping and the threshold. Never the test participant.
26 | Decision threshold | grid 0.05 to 0.95, maximise F1, centre of the plateau | Chosen on the inner validation participants, then applied unchanged to the test participant.
27 | Metrics | F1, balanced accuracy, precision, recall, specificity | Pooled over all held-out windows and reported per participant.

## Slide 5
Every Design Choice Has a Precedent (1/2)
Component | Model B | Precedent | Status
Sensors | Accelerometer X, Y, Z and optical over the temporalis | Same four AIM-2.1 channels [2]. Optical sensing on smart glasses reached F1 0.91 [8]. Temporalis activity reflects chewing [9, 1] | Established
Sampling rate | 128 Hz, the device rate | AIM-2 records at 128 Hz [1, 2]. Accuracy holds down to about 10 to 25 Hz in activity recognition [28] | Established. 32 Hz test planned
Window length | 8 s | 8 s epochs [2]. Others used 10 s [1], 15 s [3] and 5 s [4]. Window size changes results [38] | Established. 4 and 16 s sweep planned
Window label | Eating if more than 50% of the window is eating | Same majority rule [1] | Established
Annotated time only | Unannotated time is dropped, never labelled not eating | Labels come only from ground truth [1, 2] | Established
Missing samples | Excluded from the z-score, then set to 0 | No direct precedent found | Design choice, covered by pipeline tests
Normalisation | Z-score per window and per channel | Normalisation for inter-subject variation [1]. Z-normalised series are standard in time series classification [14, 15] | Established
Filtering | None. The input is not band-passed | Raw input without filtering [2]. AIM-2 used a 0.1 Hz high-pass and 3 Hz low-pass [1] | Open. Filter test planned
Input representation | Time series, not FFT magnitude | Raw time series with CNNs [2, 15, 14, 12] | Own ablation. FFT input costs 0.087 F1
Convolution trunk | Three 1D conv blocks with BatchNorm and ReLU | 1D CNNs for time series [15, 14]. Deeper conv stacks helped on AIM [2]. BatchNorm [29] | Established
Strided convolution | Stride 2 plus max pooling to shorten the sequence | Strided convolution as downsampling [36] | Established
Numbers in brackets refer to the reference slides at the end.

## Slide 6
Every Design Choice Has a Precedent (2/2)
Component | Model B | Precedent | Status
Channel attention | Squeeze and excitation on the 64 learned channels | Introduced in [17]. Used in time series classification [16] and radio signals [6] | Standard. Own ablation within noise
Attention pooling | Softmax weights over 64 time steps | Attention over time in activity recognition [18]. Attention-based pooling [19]. AIM work used global average pooling [2] | New on AIM. Within noise
Dropout | 0.3 after the shared dense layer | [31] | Established
Chew count head | Auxiliary regression, weight 0.2, training only | Multitask learning [20]. Chew counting from sensors [11] | New on AIM. Within noise
Class weighting | Per-fold inverse class frequency | Imbalanced learning [33]. Cost-sensitive training on AIM [3] | Established
Optimiser and stopping | Adam 0.001, early stopping on validation loss | [30, 34] | Established
Overlapping windows | 50% overlap for training, non-overlapping for testing | Overlap inflates results only under subject-dependent evaluation, and subject cross-validation is recommended [21] | Own ablation. +0.025 F1
Cross-validation | Leave one subject out | Used in [1, 2, 3, 4]. Subject-wise splits are required for a valid estimate [22] | Established. Lab standard
Threshold | Chosen on inner validation participants to maximise F1 | [23] | Established
Metrics | F1 and balanced accuracy lead | F1 as the headline metric [4, 2]. Balanced accuracy [37] | Established
Alignment check | Cross-correlation of chewing energy with labels | No direct precedent found | Own method, validated on synthetic offsets
Numbers in brackets refer to the reference slides at the end.

## Slide 7
Changes Since the 4/22 Proposal
Component | 4/22 proposal | Model B now
Participants | 14 | 20 (61 sessions available)
Window | 10 s, 1,280 samples | 8 s, 1,024 samples
Filtering | 0.1 Hz high-pass | None, z-score only
Conv layers | 2 (16 and 32 filters, kernels 5 and 9) | 3 (32, 64, 64 filters, kernels 9, 9, 5), strided
Channel attention | Reduction ratio 8 | Squeeze and excitation, reduction 4
Dense and dropout | Dense 16, dropout 0.2 | Dense 64, dropout 0.3
Outputs | Food only | Food plus chew count (training only)
Batch, epochs, patience | 32, 30, 5 | 64, 80, 12
Training windows | Non-overlapping | 50% overlap, tested non-overlapping
Validation | 4 folds plus 2 held-out participants | Leave one subject out
The core idea is unchanged: 1D convolutions, cross-channel attention, attention pooling and a sigmoid classifier.

## Slide 8
Priority: Fewer False Positives
Evaluation | False positives | Non-eating windows | False positive rate | Precision
4-fold | 139 | 2,328 | 6.0% | 0.876
Leave one subject out | 207 | 2,328 | 8.9% | 0.828
Approach | What it does | Precedent | Note
Precision-targeted threshold | Pick the threshold on validation that keeps the false positive rate under a set target, for example 5% | [23] | No retraining. Costs some recall
Negative examples from other datasets | Add non-eating recordings from other studies into ETS as extra negatives, split by participant | [3] reports false positives from chewing gum | Agreed at the 9/23 meeting
Cost-sensitive loss | Weight a false positive more than a false negative, or use focal loss | [3, 32] | One parameter to sweep
Signal-quality gating | Use accelerometer-only decisions when the optical signal is weak | [1] | Two-stage rule from AIM-2
Augmentation | Noise, time masking and shifts during training | [6] | Largest single gain in that paper
Goal: a clearly lower false positive rate at roughly the same accuracy.

## Slide 9
Literature Added
Paper | Why it matters here | Ref
Stankoski et al. 2024 | Optical sensors on smart glasses, ConvLSTM, F1 0.91, real-life precision 0.95 | [8]
Zhang and Amft 2018 | EMG in eyeglasses over the temporalis, free-living chewing | [9]
Bedri et al. 2020 | FitByte eyeglasses, multimodal fusion to cut false positives, F1 0.89 | [10]
Kyritsis et al. 2021 | End-to-end CNN and LSTM on raw smartwatch data | [12]
Farooq and Sazonov 2016 | Automatic chew counting, basis for the chew head | [11]
Karim et al. 2019 | Squeeze and excitation in time series classification | [16]
Murahari and Plötz 2018 | Attention over time for wearable activity recognition | [18]
Dehghani et al. 2019 | Overlapping windows and subject-independent evaluation | [21]
Saeb et al. 2017 | Why splits must be by subject | [22]
Shavit and Klein 2021, Dirgová Luptáková et al. 2022 | Transformers on wearable inertial data | [26, 27]
Zerveas et al. 2021, Haresamudram et al. 2020 | Self-supervised pretraining for sensor time series | [25, 24]
Yamane et al. 2025 | Lower sampling rates keep accuracy, supports the 32 Hz test | [28]

## Slide 10
References (1/2)
[1] A. Doulah, T. Ghosh, D. Hossain, M. H. Imtiaz, E. Sazonov, "Automatic Ingestion Monitor Version 2 - A novel wearable device for automatic food intake detection and passive capture of food images," IEEE Journal of Biomedical and Health Informatics, vol. 25, no. 2, pp. 568-576, 2021. doi 10.1109/JBHI.2020.2995473
[2] T. Ghosh, E. Sazonov, "A comparative study of deep learning algorithms for detecting food intake," Proc. 44th Annual Int. Conf. IEEE EMBC, Glasgow, 2022, pp. 2993-2996. doi 10.1109/EMBC48229.2022.9871278
[3] T. Ghosh, Y. Han, V. Raju, D. Hossain, M. A. McCrory, J. Higgins, C. Boushey, E. J. Delp, E. Sazonov, "Integrated image and sensor-based food intake detection in free-living," Scientific Reports, vol. 14, 1665, 2024. doi 10.1038/s41598-024-51687-3
[4] C. Diou, K. Kyritsis, V. Papapanagiotou, I. Sarafis, "Intake monitoring in free-living conditions. Overview and lessons we have learned," Appetite, 2022. doi 10.1016/j.appet.2022.106096
[5] M. Usman, H. Chen, "Recent trends in food intake monitoring using wearable sensors," arXiv 2101.01378, 2021.
[6] J. Yang, Y. Wang, M. Yang, H. Meng, "Signal classification based on multi-scale time-frequency transformer," Physical Communication, vol. 75, 103022, 2026. doi 10.1016/j.phycom.2026.103022
[7] S. Ikram et al., "Transformer-based ECG classification for early detection of cardiac arrhythmias," Frontiers in Medicine, vol. 12, 1600855, 2025. doi 10.3389/fmed.2025.1600855
[8] S. Stankoski, I. Kiprijanovska, M. Gjoreski, F. Panchevski, B. Sazdov, B. Sofronievski, A. Cleal, M. Fatoorechi, C. Nduka, H. Gjoreski, "Controlled and real-life investigation of optical tracking sensors in smart glasses for monitoring eating behavior using deep learning. Cross-sectional study," JMIR mHealth and uHealth, vol. 12, e59469, 2024.
[9] R. Zhang, O. Amft, "Monitoring chewing and eating in free-living using smart eyeglasses," IEEE Journal of Biomedical and Health Informatics, vol. 22, no. 1, pp. 23-32, 2018. doi 10.1109/JBHI.2017.2698523
[10] A. Bedri, D. Li, R. Khurana, K. Bhuwalka, M. Goel, "FitByte. Automatic diet monitoring in unconstrained situations using multimodal sensing on eyeglasses," Proc. CHI Conference on Human Factors in Computing Systems, 2020. doi 10.1145/3313831.3376869
[11] M. Farooq, E. Sazonov, "Automatic measurement of chew count and chewing rate during food intake," Electronics, vol. 5, no. 4, 62, 2016. doi 10.3390/electronics5040062
[12] K. Kyritsis, C. Diou, A. Delopoulos, "A data driven end-to-end approach for in-the-wild monitoring of eating behavior using smartwatches," IEEE Journal of Biomedical and Health Informatics, vol. 25, no. 1, pp. 22-34, 2021.
[13] N. Bahador, D. Ferreira, S. Tamminen, J. Kortelainen, "Deep learning-based multimodal data fusion. Case study in food intake episodes detection using wearable sensors," JMIR mHealth and uHealth, vol. 9, no. 1, e21926, 2021.
[14] H. Ismail Fawaz, G. Forestier, J. Weber, L. Idoumghar, P.-A. Muller, "Deep learning for time series classification. A review," Data Mining and Knowledge Discovery, vol. 33, pp. 917-963, 2019. doi 10.1007/s10618-019-00619-1
[15] Z. Wang, W. Yan, T. Oates, "Time series classification from scratch with deep neural networks. A strong baseline," Proc. Int. Joint Conf. Neural Networks (IJCNN), 2017, pp. 1578-1585.
[16] F. Karim, S. Majumdar, H. Darabi, S. Harford, "Multivariate LSTM-FCNs for time series classification," Neural Networks, vol. 116, pp. 237-245, 2019. doi 10.1016/j.neunet.2019.04.014
[17] J. Hu, L. Shen, G. Sun, "Squeeze-and-excitation networks," Proc. IEEE Conf. Computer Vision and Pattern Recognition (CVPR), 2018, pp. 7132-7141.
[18] V. S. Murahari, T. Plötz, "On attention models for human activity recognition," Proc. ACM Int. Symposium on Wearable Computers (ISWC), 2018. doi 10.1145/3267242.3267287
[19] M. Ilse, J. Tomczak, M. Welling, "Attention-based deep multiple instance learning," Proc. Int. Conf. Machine Learning (ICML), 2018.

## Slide 11
References (2/2)
[20] R. Caruana, "Multitask learning," Machine Learning, vol. 28, pp. 41-75, 1997.
[21] A. Dehghani, O. Sarbishei, T. Glatard, E. Shihab, "A quantitative comparison of overlapping and non-overlapping sliding windows for human activity recognition using inertial sensors," Sensors, vol. 19, no. 22, 5026, 2019. doi 10.3390/s19225026
[22] S. Saeb, L. Lonini, A. Jayaraman, D. C. Mohr, K. P. Kording, "The need to approximate the use-case in clinical machine learning," GigaScience, vol. 6, no. 5, gix019, 2017.
[23] Z. C. Lipton, C. Elkan, B. Narayanaswamy, "Optimal thresholding of classifiers to maximize F1 measure," Proc. ECML PKDD, LNCS vol. 8725, pp. 225-239, 2014.
[24] H. Haresamudram, A. Beedu, V. Agrawal, P. L. Grady, I. Essa, J. Hoffman, T. Plötz, "Masked reconstruction based self-supervision for human activity recognition," Proc. ACM ISWC, 2020. doi 10.1145/3410531.3414306
[25] G. Zerveas, S. Jayaraman, D. Patel, A. Bhamidipaty, C. Eickhoff, "A transformer-based framework for multivariate time series representation learning," Proc. ACM SIGKDD Conf. Knowledge Discovery and Data Mining, 2021. doi 10.1145/3447548.3467401
[26] Y. Shavit, I. Klein, "Boosting inertial-based human activity recognition with transformers," IEEE Access, vol. 9, pp. 53540-53547, 2021. doi 10.1109/ACCESS.2021.3070646
[27] I. Dirgová Luptáková, M. Kubovčík, J. Pospíchal, "Wearable sensor-based human activity recognition with transformer model," Sensors, vol. 22, no. 5, 1911, 2022. doi 10.3390/s22051911
[28] T. Yamane, M. Kimura, M. Morita, "Effects of sampling frequency on human activity recognition with machine learning aiming at clinical applications," Sensors, vol. 25, no. 12, 3780, 2025.
[29] S. Ioffe, C. Szegedy, "Batch normalization. Accelerating deep network training by reducing internal covariate shift," Proc. ICML, 2015.
[30] D. P. Kingma, J. Ba, "Adam. A method for stochastic optimization," Proc. Int. Conf. Learning Representations (ICLR), 2015.
[31] N. Srivastava, G. Hinton, A. Krizhevsky, I. Sutskever, R. Salakhutdinov, "Dropout. A simple way to prevent neural networks from overfitting," Journal of Machine Learning Research, vol. 15, pp. 1929-1958, 2014.
[32] T.-Y. Lin, P. Goyal, R. Girshick, K. He, P. Dollár, "Focal loss for dense object detection," Proc. IEEE Int. Conf. Computer Vision (ICCV), 2017, pp. 2980-2988.
[33] H. He, E. A. Garcia, "Learning from imbalanced data," IEEE Transactions on Knowledge and Data Engineering, vol. 21, no. 9, pp. 1263-1284, 2009.
[34] L. Prechelt, "Early stopping, but when?," in Neural Networks. Tricks of the Trade, LNCS vol. 1524, Springer, 1998, pp. 55-69.
[35] F. J. Ordóñez, D. Roggen, "Deep convolutional and LSTM recurrent neural networks for multimodal wearable activity recognition," Sensors, vol. 16, no. 1, 115, 2016.
[36] J. T. Springenberg, A. Dosovitskiy, T. Brox, M. Riedmiller, "Striving for simplicity. The all convolutional net," ICLR Workshop, 2015.
[37] K. H. Brodersen, C. S. Ong, K. E. Stephan, J. M. Buhmann, "The balanced accuracy and its posterior distribution," Proc. Int. Conf. Pattern Recognition (ICPR), 2010, pp. 3121-3124.
[38] O. Banos, J.-M. Galvez, M. Damas, H. Pomares, I. Rojas, "Window size impact in human activity recognition," Sensors, vol. 14, no. 4, pp. 6474-6499, 2014.